## Slide 1: NCP3237 PC1 Evaluation Board Guide

## Slide 2
5
5
4
4
3
3
2
2
1
D
D
C
C
B
B
A
A
VIN
EN
1.8V
1V
1.2V
2.5V
1.5V
3.3V
NA+
NA-
TO SIGN. GEN.
TRANSIENT LOAD
750K
550K
1.1M
2oz copper.
The top layer contains the main power traces for VIN, VOUT, and SW. Also on the top layer are majority of the signal traces. The top layer has dedicated ground plane for quiet analog ground that is connected to the main power ground plane at a single point. The internal layer-1 is a large ground plane and also routes signals to test points. The internal layer-2 contains an additional large ground copper area as well as an additional VIN and VOUT copper fill. The bottom layer is another ground plane with two additional traces for the output voltage feedback. The top-side ground traces are connected to the bottom and internal ground planes with multiple vias placed around the board.
The input decoupling capacitors and bootstrap capacitor are all located as close to the IC as possible. Additionally, the voltage set point resistor divider components are kept close to the IC. The voltage divider network ties to the output voltage at the point of regulation. Critical analog circuits such as the voltage set point divider, EN resistor and COMP pin are terminated to the quiet analog ground island on the top layer.
SW
PGND
Vin
EN
PG
Vout
VCC
Vin
TP7
R17 511
1
L1
1uH
RA1
DNP
1
R26 DNP
For TPS54824
1
2
J11
2
1
DNP
2 1
R1
0
For NCP3239
1
R27
2
CA1 DNP
1 2
2
Q2 2N7002LT1
3 2
2
R21
1
6.32K
2
Vout
TP5
13.7K
R12
1
2
J14
HEADER 5X2_5103308-1
4
6
8
10
1 2
3
5
7
9
R18
1
20K
2
DNP
2 1
R2
1
30K
2
C3
0.1uF
1
2
R7
30.1K
1
2
C12
0.1uF
1
2
C18
680pF
R30 0
1
C19
1nF
J13
2
1
2
1
DNP
R25
1
2
R11
150
QFN3535-18L
U1
NCP3237
15
COMP
14
FB
AGND
12
VCC
16
VIN1
2
8
PGND4
PGND6
10
7
SW2
SW1
6
BST
1
18
PGOOD
17
EN
VIN2
11
PGND1
3
4
PGND2
5
PGND3
PGND5
9
C8
47uF
J1
1
2PIN 1ROW 2
J6
2
1
R23
1
4.42K
2
TP2
C5
22uF
2.0 R3
2 1
R6 90.0K
2 1
J10R20
1
29.4K
2
R15
1
20K
2
T1
1
2
1
J16
2
C15
10uF
TP3
2
1
2
1
C7
0.1uF
1
2
1
J15
2
BST
TP11
J3
2
TP10 FB
J7 R16
1
13.3K
2
+
C13
DNP
J12
R22
1
40.2K
2
1
R8 0.0
2
R5 0.0
1
C1 C6
22uF 22uF
C9 C10 C11 47uF 47uF 47uF
TP1
TP8
J9
2
1
C2
0.1uF
2 1
T2
1
2
Q1
NTMS4801
COMP TP6
R24
1
DNP
2
R9 100K
1 2
TP12
TP4
R29 0
1
R10 10.0
TP9
+
C4
100uF
R19
1
10.0K
2
D1
GRN
1 1
2
J2
1
2
J5 R14
2
1
J8
2
1
C17
68pF
10.0K R4
1 2
R13
20K
2 1
VIN
EN
NA+
BST 2
SW
VOUT
FB
COMP
PGND
PG
1 PG
AGND
FSET
FSET 13
FSET
R28 0
1 2 FSET
2 PG
2 EN
Schematic

## Slide 3
Item | Quantity | Reference | Value | PCB Footprint | MFG P/N | MFG | DESCRIPTION
1 | 1 | CA1 | DNP | SMC0402 |  |  | 
2 | 3 | C1,C5,C6 | 22uF | C0805 | C2012X5R1E226M125AC | TDK | CAP CER 22UF 25V X5R 0805
3 | 4 | C2,C3,C7,C12 | 0.1uF | SMC0603 | 06033C104KAT2A | AVX | CAP, SMT, 0603, 0.1uF, 25V, 10%
4 | 1 | C4 | 100uF | MU_10 | A767MU107M1VLAE029 | KEMET | CAP, SMT, MU_10, 100uF, 35V, 20%
5 | 4 | C8,C9,C10,C11 | 47uF | C0805 | GRM21BR61A476ME15L | MURATA | CAP CER 47UF 10V X5R 0805
6 | 1 | C13 | DNP | MU_10 | A767MU107M1VLAE029 | KEMET | CAP, SMT, MU_10, 100uF, 35V, 20%
7 | 1 | C15 | 10uF | C0805 | C2012X5R1A106M085AB | TDK | CAP CER 10UF 10V X5R 0805
8 | 1 | C17 | 68pF | CSMI_0603 | CC0603JRNPO9BN680 | Yageo | CAP CER 68PF 50V C0G/NPO 0603
9 | 1 | C18 | 680pF | CSMI_0603 | 885012206082 | Würth Elektronik | CAP CER 680PF 50V X7R 0603
10 | 1 | C19 | 1nF | CSMI_0603 | GRM1885C1H102JA01D | Murata Electronics | CAP CER 1000PF 50V C0G/NP0 0603
11 | 1 | D1 | GRN | D0805 | LTST-C170GKT | LITE-ON | LED GREEN CLEAR SMD
12 | 14 | J1,J2,J3,J5,J6,J7,J8,J9,J10,J11,J12,J13,J15,J16 | 2PIN 1ROW | JTHI_HDR1R2PS | 10/22/2021 | MOLEX | CONN HEADER VERT 2POS 2.54MM
13 | 1 | J14 | HEADER 5X2_702471051 | 702471051 | 702471051 | Molex | CONN HEADER R/A 10POS 2.54MM
14 | 1 | L1 | 1uH | 7_10X6_50X3_00MM | SPM6550T-1R0M100A | TDK | FIXED IND 1.09UH 14.1A 5.2 MOHM
15 | 1 | Q1 | NTMS4801 | SO8_PTDSON8_SO8FL_COMBO_8MIL | NTMS4801NR2G | ON SEMICONDUCTOR | MOSFET N-CH 30V 7.5A 8-SOIC
16 | 1 | Q2 | 2N7002LT1 | QSMI_SOT23 | 2N7002LT1G | ON SEMICONDUCTOR | MOSFET N-CH 60V 0.115A SOT-23
17 | 1 | RA1 | DNP | SMR0402 |  |  | 
18 | 2 | R1,R2 | DNP | RSMI_2512 |  |  | 
19 | 1 | R3 | 2 | SMR0603 | ERJ-3GEYJ2R0V | Panasonic | RES SMD 2 OHM 5% 1/10W 0603
20 | 2 | R4,R19 | 10.0K | SMR0603 | CRCW060310K0FKEA | Vishay Dale | RES SMD 10K OHM 1% 1/10W 0603
21 | 2 | R5,R8 | 0 | SMR0603 | CRCW06030000ZSTB | DALE | RES, SMT, 0603, 0, 1/16W, 5%
22 | 1 | R6 | 90.0K | SMR0603 | PATT0603E8982BGT1 | Vishay Thin Film | RES SMD 89.8KOHM 0.1% 0.15W 0603
23 | 1 | R7 | 30.1K | SMR0603 | CRCW060330K1FKEA | DALE | RES, SMT, 0603,30.1K, 1/10W, 1%
24 | 1 | R9 | 100K | SMR0603 | CRCW0603100KFKEA | Vishay Dale | RES SMD 100K OHM 1% 1/10W 0603
25 | 1 | R10 | 10 | SMR0603 | CRCW060310R0FKEA | Vishay Dale | RES, SMT, 0603, 10.0, 1/10W, 1%
26 | 1 | R11 | 150 | SMR0603 | CRCW0603150RFKEA | Vishay Dale | RES SMD 150 OHM 1% 1/10W 0603
27 | 1 | R12 | 13.7K | SMR0603 | CRCW060313K7FKEA | Vishay Dale | RES SMD 13.7K OHM 1% 1/10W 0603
28 | 3 | R13,R15,R18 | 20K | SMR0603 | CRCW060320K0FKEA | Vishay Dale | RES 20K OHM 1% 1/10W 0603
29 | 1 | R14 | 30K | SMR0603 | CRCW060330K0FKEA | Vishay Dale | RES SMD 30K OHM 1% 1/10W 0603
30 | 1 | R16 | 13.3K | SMR0603 | CRCW060313K3FKEB | Vishay Dale | RES SMD 13.3K OHM 1% 1/10W 0603
31 | 1 | R17 | 511 | SMR0603 | CRCW0603511RFKEB | Vishay Dale | RES, SMT, 0603, 511, 1/10W, 1%
32 | 1 | R20 | 29.4K | SMR0603 | CRCW060329K4FKEA | Vishay Dale | RES SMD 29.4K OHM 1% 1/10W 0603
33 | 1 | R21 | 6.32K | SMR0603 | CRCW06036K34FKEA | Vishay Dale | RES SMD 6.34K OHM 1% 1/10W 0603
34 | 1 | R22 | 40.2K | SMR0603 | CRCW060340K2FKEA | Vishay Dale | RES SMD 40.2K OHM 1% 1/10W 0603
35 | 1 | R23 | 4.42K | SMR0603 | CRCW06034K42FKEA | DALE | RES SMD 4.42K OHM 1% 1/10W 0603
36 | 3 | R24,R25,R26 | DNP | SMR0603 | - | - | 
37 | 4 | R27,R28,R29,R30 | 0 | SMR0603 | CRCW06030000ZSTB | DALE | RES, SMT, 0603, 0, 1/16W, 5%
38 | 12 | TP1,TP2,TP3,TP4,TP5,TP6,TP7,TP8,TP9,TP10,TP11,TP12 | TP | TPTHI_100R76 | 2305-2-00-01-00-00-07-0 | MILL-MAX | TESTPOINT, TH, 100R76, TERMINAL, TURRET
39 | 2 | T1,T2 | 2PIN/TERM BLK | TERM_BL_2PS | 39889-0042 | Molex | CON, TH, 2PIN, TERMINAL BLOCK
40 | 1 | U1 | NCP3237 | NCP3239 | NCP3237 | ON SEMI | 
41 | 1 | NCP3237_EVB_REVB_PCB | 305-PD-20-0313 |  |  |  | 
BOM

## Slide 4: Enable and PGOOD
To enable with Vin divider, connect jumper to J15
To have PGOOD pull-up to VCC, connect jumper to J16

## Slide 5: Vout Select
Select output voltage by connecting the corresponding jumper
J5 for Vout = 1V
J6 for Vout = 1.2V
J7 for Vout = 1.5V
J9 for Vout = 1.8V
J11 for Vout = 2.5V
J13 for Vout = 3.3V

## Slide 6: Switching Frequency Select
Select switching frequency by connecting the corresponding jumper
J8 for Fsw = 1.1MHz
J10 for Fsw = 750kHz
J12 for Fsw = 550kHz

## Slide 7: Optional on Indicator LED
To add the optional indicator LED for when the part is on, connect jumper to J3

## Slide 8: EVB Comp Loop
Bode 12Vin, 1.8Vout, Fsw=550kHz, 8A PM=49 deg, GM=20 dB, BW=61.7kHz

## Slide 9: EVB Comp Loop
Load Transient Response 1.8Vout, 550kHz. 2 to 4A step