## Slide 1: NCP730 150mA 38V Technical Presentation
Ivan Miksanek, Tim Hedquist
t.hedquist@onsemi.com
June 2022

## Slide 2: NCP730 – Main Features
Wide input voltage range 2.7V – 38V
Wide output voltage range 1.2V – 24V (both FIX and ADJ)
High output voltage accuracy ±1% (-40 to 85degC); -1/+2% (-40 to 125ºC)
Output current up to 150mA (200mA peak)
Low dropout voltage: typ. 290mV @ 3.3V, 150mA / 245mV @ 5V, 150mA
PG output device option (B version)
Stable with 1uF – 100uF output ceramic capacitor
Built-in soft start circuit
Low dropout (dropout depends on voltage variant, load current and temperature)
Low quiescent current, typ. 1.3uA (A version – no PG), 1.8uA (B version – with PG)
Very good transient response and PSRR (note this is 1uA device!)
Two industry-standard packages TSOP−5 and WDFN6 2x2 mm

## Slide 3: NCP730 to TI TPS709 Comparison
Why use the NCP730?
  VIN_max up to 38V; covers 24VAC common wire requirements
  Vout range from 1.2V – 24V
  Faster transient response
  Available in fixed & adjustable configurations
  Power Good (PG) is available
  Available in TSOP5 & WDFN6_2x2
  Direct drop-in, P2P, to TPS709 with improved performance!

## Slide 4: NCP730 – Max Output current vs. Input voltage
WDFN-6 package
TSOP-5 package
Max. output current shown at these graphs is computed from max. power dissipation (PCB, TA and TJ dependent) and desired output voltage version by equation: IOUT-MAX = PDIS-MAX / (VIN – VOUT-NOM) at TA=25°C and TJ=125°C, for JEDEC test board with Cu area 650mm2, thickness 1oz. It means that on different customer’s PCB and/or different TA and TJ inputs the graphs will look different.

## Slide 5: NCP730 – Basic Applications, Block Diagrams, & Pinouts

## Slide 6: Start-up by VIN (slow) - NCP730-ADJ-3.3V
CADJ1 = 0pF, COUT = 1uF
CADJ1 = 100pF, COUT = 1uF
CADJ1 = 1nF, COUT = 1uF
Common conditions: Vin=0V->40V, Iout=100mA
Purpose of this slide is to show the influence of CADJ1 (feed-forward) capacitor and COUT capacitor to speed of VOUT rise/fall after start-up by VIN.
Note that VIN and VOUT scales are different (not important in this case).
No overshoot of VOUT observed.
CADJ1 = 1nF, COUT = 47uF
VOUT
VIN
VOUT
VIN
VOUT
VIN
VOUT
VIN

## Slide 7: Start-up by VIN (medium & slow) - NCP730-15V
VIN ramp times tr=tf=600us (medium)
VIN ramp times tr=tf=6ms (slow)
Vin=0V->40V, Iout=100mA, Cout=1uF
No overshoot of VOUT observed.
VOUT
VIN
VPG
VOUT
VIN
VPG

## Slide 8: Start-up by VIN (fast) - NCP730-3.3V
VOUT
VIN
VPG
IIN
ILOAD=100mA
RPG=10kW
COUT=47uF
Here VPG copies VOUT because PG is connected to OUT pin by RPG resistor.
PG indicates the power is OK
Here VPG is almost 0V (current from OUT pin through external RPG causes voltage drop at internal PG’s N-MOS).
PG indicates power is NOT ok.
Here the LDO limits output current to IOLIM level.
Here the LDO is in regulation.
The VOUT rise speed is given by COUT, IOLIM and ILOAD. COUT is charged by shown IIN minus ILOAD (100mA). Internal soft start is normally faster.
4.3V
0V
3.3V
Current pulse caused by CIN charging
IIN=ILOAD=100mA
COUT=47uF
VOUT
VIN
VPG
IIN
ILOAD=100mA
RPG=10kW
COUT=47uF
Here VPG copies VOUT because PG is connected to OUT pin by RPG resistor.
PG indicates the power is OK
Here VPG is almost 0V (current from OUT pin through external RPG causes voltage drop at internal PG’s N-MOS).
PG indicates power is NOT ok.
Here the LDO is in regulation.
The VOUT rise speed is given internal soft start.
Current pulse caused by CIN charging
4.3V
0V
IIN=ILOAD=100mA
3.3V
COUT=1uF

## Slide 9: NCP730-5.0V – Quiescent current (IQ), IOUT=0mA
GND pin current @ 150mA (ATE)
Quiescent current, IQ [uA]
VIN=38V over temp

## Slide 10: NCP730 Ground Current
IOUT=150mA over temperature
Ground current vs. Output current
Ground current, IGND [uA]
Output current, IOUT [mA]
TJ=25°C

## Slide 11: NCP730-5.0V – Dropout voltage over temperature
Dropout voltage, VDO [mV]

## Slide 12: PSRR – NCP730ASN330 vs TPS70933, VIN=VAR, IOUT=10/100mA

## Slide 13: PSRR - Comparing VIN to Cout
COUT=1/10uF, VIN=17V, IOUT=10/100mA
COUT=10uF, VIN=VAR, IOUT=10/100mA

## Slide 14: Load transients – Vout=15V
Cout=1u
Vin=15.5V,Vout=15V, Iout=1-150mA, tr=tf=1us
Cout=10u
Cout=22u
Cout=50u
-120mV / +70mV
-0.80% / +0.47%
-110mV / +70mV
-0.73% / +0.47%
-100mV / +60mV
-0.66% / +0.40%
-44mV / +28mV
-0.29% / +0.19%
VOUT
IOUT
VIN
VOUT
IOUT
VIN
VOUT
IOUT
VIN
VOUT
IOUT
VIN
ADJ-15V Cadj1=100p
ADJ-15V Cadj1=1n
50mV/div
-90mV / +40mV
-0.60% / +0.27%
-85mV / +40mV
-0.57% / +0.27%
VOUT
IOUT
VIN
VOUT
IOUT
VIN
ADJ-15V, Cout=1uF,
(various CADJ1)

## Slide 15: NCP730 vs TPS709 – Single Load Transients zoom of NCP730
NCP730 3.3V – Cout=1u (used minimal)
TPS709 3.3V – Cout=2u (used minimal)
Iout=1-150mA, tr=tf=1us – same conditions and NOT the same scale
Comments: NCP730 is significantly better than TPS709
-435mV / +370mV
-350mV / +350mV
-310mV / +260mV
-310mV / +260mV
-310mV / +270mV
Is in dropout here
Vin=3.8V
Vin=4.3V
Vin=5.3V
Vin=12V
Vin=24V
Vin=3.8V
Vin=4.3V
Vin=5.3V
Vin=12V
Vin=24V
-122mV / +65mV
-120mV / +55mV
-115mV / +53mV
-114mV / +52mV
-115mV / +53mV

## Slide 16: Line transients – NCP730-3V3, COUT=1uF, IOUT=100mA
Vin=3.3-4.3V
tr=tf=1us
Vin=3.6-4.6V
Vin=3.8-4.8V
Vin=4.3-5.3V
Vin=5.3-6.3V
Vin=8.3-9.3V
Vin=4.3-9.3V
+500mV / -0mV
Note: from dropout to regulation
+24mV / -13mV
+14mV / -10mV
+9.0mV / -7.5mV
+4.0mV / -3.0mV
+2.0mV / -2.0mV
+25mV / -19mV
VOUT
VIN
VOUT
VIN
VOUT
VIN
VOUT
VIN
VOUT
VIN
VOUT
VIN
VOUT
VIN

## Slide 17: NCP730 – 38V, 150mA, 1uA Iq LDO with Power Good
Fixed & Adjustable Voltage Options Available: 1.2V to 24V
±1% Accuracy @ Tj : -40 ~ +85ºC
290mV typical dropout @ 150mA of output current, 3.3Vout
Short Circuit Protection, Thermal Shutdown Protection
Stable with 1uF ceramic capacitor
2.7V to 38V input voltage
Ultra-Low Iq : 1µA typ
Built-in Soft Start Circuit
Power Good function (Ver B)
Can support multi-cell battery application
Extend battery life / save power
Can suppress inrush current to protect IC
Can reset MCU to avoid malfunction
The NCP730 is a next generation CMOS LDO regulator designed for up to 38V input voltage and 150mA output current. Designed to meet the requirements for industrial wide-input voltage circuits. The NCP730 device provides ultra−low quiescent current of only 1uA, which makes this device ideal solution for battery powered application. Output voltage can be set from 1.2 to 24V, adjustable or fixed. The device also offer excellent load/line transient regulation and output Power Good function to reset MCU. The device is available in TSOP-5 and WDFN-6 packages.
Other Features
Ordering & Package Information
Market & Applications
Unique Features
Benefits
Value Proposition: Wide-Input Voltage, Low Iq, Low Dropout
Application Data (WDFN-6)
Datasheet: Now
Samples: Now
Release to Production: Now
Battery-Powered Power Tool and Equipment
Smart Metering, Smoke Detector
Industrial Automation, Home Automation
IT, Home Appliances
Combination Arc-Fault Circuit Breakers (CAFI)
Power Good function for MCU reset
Wide input range
Enable pin. Shutdown current ~100nA
WDFN-6 (2*2)
19

## Slide 18: Thank You