## Slide 1: Drive Module System Solution

## Slide 2
Video Processor
LDO
NCV8163 ~ 37mW
12.0V
~ 1.7W
Buck
NCV890430
393mW***
3.0V
1.8V
Buck
NCV6324 ~33mW
1.2V
Buck
NCV6324 ~ 68mW
2.8V
Image Sensor + Power Supply + IR LED driver
Connector
RAW data
LED Flash
LED Driver
NCV30161
PWM Dimming
200uS to 1mS pulse, period 16.6 mS or 20 mS
12.0V 2A
IR LED
driver board
Smart FET
NCV84160
Smart FET
NCV47822
6V/3A/1mS max
E2PROM
CAV24C64
SFH4725
SFH4727
VDD/V
DD_PHY 189mA
VAA/VAAPIX 70mA
VDDIO 177mA
Sensor
AR0144
AR0135
457mW

## Slide 3: IR LED driver
LED flashlight DC current setting：
ILED=200mV/Rsense
Smart FET
NCV84160
Optional current source
Flashlight duration：200uS to 1mS
4.7uH
Average input power 1.1W
LED driver fault diagnosis：
When Flash(DIM) is high, the LED flashlight current is high also, more than 20mA. The constant current source can be turned off immediately.
When PWM low, no current through LED lamp, the input current is low from DC/DC converter. To turn on constant current source to avoid fault diagnosis.
How to control pulse for flashlight?
Change R8 to 0.1uF capacitor, change C5 to diode. To realize PWM control by differential method of input pulse.

## Slide 4
Features
Benefits
NCV30161MNWTXG
Package– 3mm x 3mm DFN10 with wettable flanks
NCV30161 - Buck Regulator for Driving High Power LEDs
VIN Range 6.3 V to 40 V
Short LED Shutdown Protection
No Control Loop Compensation Required
Adjustable LED Current
Single Pin Brightness and Enable/Disable Control Using PWM
Supports All−Ceramic Output Capacitors and Capacitor−less Outputs
Thermal Shutdown Protection
Capable of 100% Duty Cycle Operation
Tj = -40C to 125C (Grade 1)
AECQ100 Qualified and PPAP capable
The NCV30161 is a hysteretic step−down, constant−current driver for high power LEDs. Ideal for automotive, industrial and general lighting applications utilizing minimal external components.
Typical Application diagram & Package info
Ordering info & Support
Benefits
Hysteretic control provides good power supply rejection and fast response during load transients
Dedicated PWM input (DIM/EN) enables a wide range of pulsed dimming
Uses smaller external components minimizing space and cost.
Protection features include resistor−programmed constant LED current, shorted LED protection, under−voltage and thermal shutdown.