## Slide 1: NCP1250 SIMPLIS MODELS & SIMULATION BENCHES
September 2011

## Slide 2: GOAL
PROVIDE NCP1250 MODELS AND SIMPLIS ( v6.1) BENCHES
FOR TRANSIENT AND AC ANALYSIS
TRANSIENT
SIMULATION
Startup, soft start, short circuit , ovp ,ocp…
Realistic waveform (parasitics effects)
POP & AC
SIMULATION
Open Loop Bode Plots
Gain Margin , Phase Margin , X-over Freq …
Clock Jittering effect , FFT …

## Slide 3: NCP1250_SIMPLIS.zip
1/ Unzip the file named NCP1250_252_SIMPLIS.zip in a folder
2/ Check the content of the folder after reading the following slides
3/ After reading the following slides and being aware of what is what
you can double click on any .sxsch file, run a SIMPLIS simulation
and plot any waveform you want to see.

## Slide 4: SIMPLIS SCREEN SHOT
SCHEMATIC
WINDOW
F11
WINDOW
NCP1250
MODEL
NCP1250
SYMBOL

## Slide 5: NCP1250 MODEL
OTHER NCP1250 VERSIONS ( 25A,25C,25D) TO BE PROVIDED UPON REQUEST
NCP1250_252.txt for transient simulation w/ or w/o parasitics
NCP1250_252_AC.txt for AC simulation
NCP1250_252_JIT.txt for transient simulation including CLK jitter
NCP1250_252_JIT.txt can not be used for AC simulation
NCP1250_252.txt can not be used for AC simulation (POP was not converging)
NCP1250_252_AC.txt works on Tran simulation but
protection circuits have been disabled to help AC simulation
NCP1250 MODELS ( ASCII FORMAT) ARE SPECIFIED IN THE F11
WINDOW USING THE .INCLUDE STATEMENT
e.g. .INCLUDE NCP1250_252.txt

## Slide 6: SIMULATION BENCHES
NCP1250_252_TR_Bench_fast.sxsch
.INCLUDE NCP1250_252.txt (F11 WINDOW)
This bench is set to run fast transient simulations .
The NCP1250_252 model includes all the features but the CLK
jittering .
The application schematic does not includes parasitics
capacitance nor inductances and no snubbers, resulting
in very fast transient simulation.
MODEL
BENCH

## Slide 7: SIMULATION BENCHES
NCP1250_252_TR_Bench.sxsch
.INCLUDE NCP1250_252.txt (F11 Window)
BENCH
MODEL
This bench is set to run transient simulations showing
the details of signal ringing due to parasitic capacitors
and inductors and how the ringings are damped by the snubbers.
The NCP1250_252 model includes all the features but the CLK jittering .
The application schematic does include parasitic
capacitances and inductances as well as snubbers.
The results are very realistic but transient simulation is slow.

## Slide 8: SIMULATION BENCHES
NCP1250_252_TR_Bench_wclkjitter.sxsch
.INCLUDE NCP1250_252_JIT.txt (F11 WINDOW)
BENCH
MODEL
This bench is set to run transient simulations showing
the details of signal ringing due to parasitic capacitors
and inductors and how the ringings are damped by the snubbers
the clk jittering is also included in the NCP1250_252 model.
The application schematic does include parasitic
capacitances and inductances as well as snubbers.
The results are very realistic but transient simulation is slow.
FFT can be run on the simulated waveforms to see the effect
of the clk jitter on spectrum spreading.

## Slide 9: SIMULATION BENCHES
NCP1250_252_AC_Bench.sxsch
.INCLUDE NCP1250_252_AC.txt ( F11 WINDOW)
BENCH
MODEL
This bench is set to run AC simulations with a bench w/o parasitics
Protection circuitry ( OVP , OCP …) of the NCP1250_252 model have
been removed in order to have the POP to converge.

## Slide 10: SUPPORT
Models Developed by Jose Capilla ON Semiconductor Tel: +33 5 3461 11 25
email: jose.capilla@onsemi.com Visit our Web site: www.onsemi.com