## Slide 1
Control Loop Design and Easy Verification Method
Public Information © onsemi 2022
Didier Balocco

## Slide 2: Introduction
The objective of this paper is to demystify loop simulations and loop measurements.
A simple method will be introduced and it can be applied to any loop with analog or digital control.
This method will use very simple equipment.
This paper will not cover simulation models creation but only how to use them.

## Slide 3: Content
Introduction (Done).
Loop Theory and Stability Criteria.
Characterization.
Simulations.
Measurement Method.
Loop Optimization.
Conclusion.

## Slide 4: Loop Theory and Stability Criteria
Public Information © onsemi 2022
(Very brief and simple)

## Slide 5: Loop Theory: System Block Diagram
Any loop can be modeled as:
Where H is the Plant to control, K the measurement divider and C the compensator
Reference
Error
Drive
Output
C
H
Measurement | K

## Slide 6: Loop Theory: System Equations
We can write the following equations:
 Error  Reference  K Output

 Output  C H  Error
Solving those equations gives:
Output  H C Reference
1 H  K C
Reference
Error
Drive
Output
Measurement
C
H
K

## Slide 7
Loop Theory: System Equations
Normally, in the compensator C, we place an integrator. In this case, the static gain (or dc gain) is infinite. Thus:
0
In dc, we get the output equation equal to :
Lim C()  
K
Output  1 Reference
Reference
Error
Drive
Output
Measurement
C
H
K

## Slide 8
Loop Theory: System Equations
We can derive the Measurement versus Error, we get:
We can derive the Measurement versus Reference, we get:
H  K C
Measurement  Reference 1 H  K C
Measurement  H  K C Error
Reference
Error
Drive
Output
Measurement
C
H
K

## Slide 9
Loop Theory: System Equations
I will define the following terms:
− Closed-loop equation :
− Open-loop equation :
We have the following relations:
and
1 T
T
S 
1S
S
T 
H  K C
S 
1 H  K C
T  H  K C
Reference
Error
Drive
Output
Measurement
C
H
K

## Slide 10: Loop Theory: Stability Criteria
The closed-loop is unstable if the denominator equals zero.
When it happens,
  The system oscillates or saturates.
1 H  K C  0  H  K C  1
Reference
Error
Drive
Output
Measurement
C
H
K

## Slide 11: Loop Theory: Stability Criteria
Nyquist was the first to work on system stability analysis and loops.
He defined the first stability criteria:
− In the imaginary plan, moving on the open-loop curve from a low frequency f1 to a high frequency f2, to ensure stability, we should pass around the -1 and leave the -1 point on the left-hand side.
− If it is on the right-hand side, the system is unstable.

## Slide 12: Loop Theory: Stability Criteria
Stable system curve:
Unstable system curve:
Real Axis
Imaginary
Axis
f1
f1<f2
f2
-1
f1<f2
f2
Real Axis
-1
f1
Imaginary
Axis

## Slide 13: Loop Theory: Margins Definitions
Phase Margin:
− Phase difference between the crossover point (at 0 dB) of the open-loop transfer function magnitude and -180°.
The crossover point should be single.
Gain Margin :
− Opposite of the gain when the transfer function phase is equal to -180°.

## Slide 14: Loop Theory: Margins definitions
f1
f2
f1<f2
Gain Margin
Phase Margin
-1
Imaginary
Axis
Real Axis
Margins in Nyquist: • Margins in Bode:
Gain
Phase
f
f
-180°
Phase Margin
Gain Margin
f1
f2

## Slide 15: Loop Theory: Margins definitions
In Black-Nichols:
− Vertical axis is the Gain,
− Horizontal axis is the Phase.
Margins are easy to measure:
− Horizontally for the Phase,
− Vertically for the Gain.
Phase
Gain
-180°
Phase Margin
Gain Margin
f1
f2
-1

## Slide 16: Loop Theory: Black-Nichols Advantages
Black-Nichols diagrams are very useful when gain varies (e.g. with an optocoupler in the return path).
In this case, the curve shifts up or down.
So when the gain changes, it is very easy to evaluate how much phase margin will remain.

## Slide 17: Loop Theory: Black-Nichols Advantages
Phase
Gain
CTR Min
CTR Average
Phase
-180°
CTR Max
Min
Max Phase Margin
Margin
-1
Min Gain Margin
Max Gain Margin
You may need to select a different CTR optocoupler when you measure open-loop curves and display them in a Black-Nichols diagram.

## Slide 18: Characterization
Public Information © onsemi 2022
How to obtain the plant or system transfer function ?

## Slide 19: Characterization: Principle
When we don’t have the Plant equation:
− We can simulate or measure it.
The obvious way is to work with the system in open-loop.
Problems (mainly when measuring a real system):
− The transfer function depends on the operating point.
− Any noise (or self-heating) during measurement can change it…
  The system can saturate and not behave in linear region.

## Slide 20: Characterization: Principle
We will simulate or measure the system in closed-loop to have the operating point automatically set by the loop.
We need a way to open the loop to obtain the transfer function…by simulation or measurement.
− We need a kind of mux to maintain the loop around its dc operating point and inject the ac measurement/simulation signal.
  We can use a simple adder.

## Slide 21
Characterization: Principle
The system to characterize + the adder can be modeled with the following block diagram:
− Where  is the injected or added ac signal to the loop.
Reference Error
Drive
Output
C
H
K

Return =
Measurement
Addition

## Slide 22: Characterization: Principle
The measurement system equations are:
After solving, we get:
Output  H C Reference  H C 
1 H  K C 1 H  K C
 Error  Reference  Addition

Drive  C Error

 Output  H  Drive
 Return  K Output

 Addition   Return
Reference
Error
Drive
Output
C
H
K

Return =
Measurement
Addition

## Slide 23
Loop Measurement System Equations
Considering ac signals only in previous system,
►
“− Closed-Loop”
►
“− Open-Loop”
It is almost what we are looking for…Open- or Closed-Loop.

we can obtain the following equations around the adder:
Return  H  K C
1 H  K C
Return  H  K C Addition
Reference
Error
Drive
Output
C
H
K

Return =
Measurement
Addition

## Slide 24: Characterization: Discussion
In theory, in this block diagram, the injection point has no influence on the loop being measured or simulation.
− It can be placed anywhere in the loop.
There are 3 ways to make a Mux/Adder to inject  in the loop :

Addition
Return
Return
Addition

Return
Addition


## Slide 25
Characterization: Discussion
First solution :
− For simulation: a simple voltage source
− For measurement: using a transformer for galvanic isolation.
Second solution :
− It is the same principle like in RF,
when power and RF use the same coaxial cable.
Return
Addition

Return
− For simulation only: as the crossover frequency is lower than in RF,
we can use a 1-kF capacitor and 1-kH inductor to have enough bandwidth and separate DC and AC signals.
Addition


## Slide 26: Characterization: Discussion
Third solution :
− For simulation: adder are available in libraries
− For measurement: using an adder with unity gain made with an operational amplifier and resistors.

Addition
Return

## Slide 27: Characterization : Discussion
Output

Addition
Return

## Slide 28: Characterization: Practical Measurement Aspects
We need to inject the signal WITHOUT “changing” the system characteristics.
− If measurement or simulations depend on the injection level, injection setup or are not reproducible;
  results are not valid.
In practice, impedance matching can influence the measurement results.

## Slide 29: Characterization: Practical Measurement Aspects
Impedance matching: here is the best practice :
Before
After
ZOut
ZIn
ZOut
ZIn
Injection function

Before
After
ZOut
ZIn
Injection
Point

## Slide 30: Characterization: Practical Measurement Aspects
Using a low output impedance point, it is easier :
ZIn
Injection
Point
Before After Before
Valid if :
− The output impedance is lower than 1 
− The input impedance is higher than 1 k.
After
ZIn
Injection function


## Slide 31: Characterization: Practical Measurement Aspects
The best injection point is between : the op-amp output and the opto-coupler.
The output impedance could be considered equal to zero.
Output

## Slide 32: Characterization: Practical Measurement Aspects
This point is relatively close to a zero-ohm output impedance also.
So, it can be used.
In theory, it depends on impedance ratio.
− If the ratio is bigger than 1/1000,
we get less than 0.1% error.
Output

## Slide 33: Characterization: Discussion
For measurements, we need to keep the system in the linear region.
− The injected signal  should be small.
− BUT it should be large enough to limit noise impact on measurement accuracy.
  If results depend on  amplitude, the system doesn’t operate in the linear region.
− Averaging (on digital scope) can be implemented to filter noise.

## Slide 34: Simulations
Public Information © onsemi 2022
With SIMetrix/SIMPLIS

## Slide 35: Simulations: Setup
This part will use SIMetrix/SIMPLIS (the free version works).
Models are explained in papers and books like:
− “Switch-Mode Power Supplies: SPICE Simulations and Practical Designs” / McGraw-Hill, 2014, 2nd edition
− “Designing Control Loops for Linear and Switching Power Supplies: A tutorial Guide” / Artech House Publishers
  from Christophe Basso
Models are available as libraries in web sites, like:
− http://cbasso.pagesperso-orange.fr/Spice.htm

## Slide 36
Simulations : Model
Here is the schematic for the average Voltage-Mode PWM Switch auto- toggling between CCM & DCM:

## Slide 37: Simulations: First Example
Here is a buck converter:
Here are the results:
Addition
Return
Return
Addition
 H  K C

## Slide 38: Simulations: First Example
Changing the measurement setup, Measuring between Output (instead of return) and the addition point,
We have the plant:
Addition
Out
H 
VOUT
Addition

## Slide 39: Simulations: More Results with “Same” File…
For simplicity, we use the following hierarchical/block schematic :

## Slide 40: Simulations: More Results with “Same” File…
For simplicity, we use the following hierarchical/block schematic :

## Slide 41: Simulations: More Results with “Same” File…
Output impedance:
Here is the setup: • Here are the results:
OUT
Z  VOUT
I
OUT

## Slide 42: Simulations: More Results with “Same” File…
Input rejection ratio (PSRR):
Here is the setup: • Here are the results:
PSRR  VOUT
VIN

## Slide 43: Simulations: More Results with “Same” File…
Input impedance:
Here is the setup: • Here are the results:
IN
Z  VIN
I
IN

## Slide 44: Simulations: More Results with “Same” File…
Reference transient or tracking:
Here is the setup: • Here are the results:

## Slide 45: Simulations: More Results with “Same” File…
Load and Input transients:
Load transient setup: • Input transient setup:

## Slide 46: Measurement Method
Public Information © onsemi 2022
With an Adder

## Slide 47
Measurement Method
The adder is made with an operational amplifier:
50Ω
Return
Addition
ε
R
R
R
NCS2005
NCS2005
R
R=10kΩ or 1kΩ
To prevent dc level in the  generator, we use a follower.

## Slide 48: Measurement Method
onsemi NCS2005 characteristics:
− 8-MHz bandwidth,
− Rail to rail,
− 2.8 V/µs slew rate,
− Supply voltage from 2.2 V up to 38 V,
− Low offset: 0.2 mV,
− Low supply current: 1.3 mA
− Maximum output current: 20 mA.

## Slide 49: Measurement Method
Advantages :
− Large bandwidth,
  Several hundreds of kHz with NCS2005
− Very good linearity,
− Adder is a low-pass filter.
It always introduces a positive phase shift
  The real phase margin is always equal or higher that the measurement.
Cautions :
− The adder cannot be placed anywhere in the loop.
  Only in the small-signal path.
− The amplifier needs a positive (& negative) supply.
− The adder ground NEEDS to be connected to the plant ground.

## Slide 50: Measurement Method
To avoid distortion,  should be small.
− Generally 20 mV rms is the minimum to use,
− Maximum 100 mV peak to peak.
Compensate probes before measurement.
Measurements are done in a very noisy environment :
− Use scope averaging more than 16 times,
− Limit scope bandwidth to 20 MHz
− Synchronize the scope and the generator.

## Slide 51
Output
Measurement Method
Here is the setup with the adder board :

## Slide 52
Output
Measurement Method
Here is the setup with the adder board :
Video Tutorial :
https://www.onsemi.com/video/easy-control-loop-measurement-and- verification-example-board-used-fan65005-gevb-

## Slide 53: Measurement Method
To measure a loop, the converter must be stable.
In order to begin, use a high-value capacitor in the compensator op-amp feedback path.
− This will slow down the transient response, but the loop will be stable.
− Increase also the soft-start duration if needed.
Due to modulator sampling effect, the maximum measurement frequency should be lower than half of the switching frequency.

## Slide 54: Measurement Method
Fast method to verify stability criteria
− When Addition and Return exhibit same amplitude:
  This is when we are at the crossover frequency, the open loop gain is 0 dB,
  The phase shift between them represents the Phase Margin.
− When Addition and Return are in phase :
  The system open-loop phase is -180°,
  The gain between them is the Gain Margin.
We can also use a network analyzer for an automatic measurement of the open- loop transfer function.

## Slide 55: Loop Optimization
Public Information © onsemi 2022
Using a Math Software Program

## Slide 56
Loop Optimization: Measurement
•
Here an open-loop measurement
obtained with a network analyzer.
100
103
104
105
 40
 20
0
20
40
 180
 135
 90
 45
0
Gain (dB) Phase (°)
Gain(dB
)
Frequency (Hz)
Phase (°)

## Slide 57: Loop Optimization: Measurement Feedback
Here is the low-bandwidth feedback (−K・C) used for this measurement:
RH=19.75 kΩ RB=10 kΩ CA=100 nF RE=10 kΩ RS=4.75 kΩ CS=22 nF
We can now extract the plant H transfer function…
Output
CS
RS
RB
RH
RE
CA
100dB/1MHz

## Slide 58: Loop Optimization: Plant Transfer Function
 30
 20
 10
0
10
20
Plant Gain (dB)
Gain(dB)
 200
 150
 100
 50
0
50
Plant Phase (°)
Phase (°)
100 | 10 3 Frequency | 10 4 | 105 | 100 | 103 | Frequency | 104 | 105
 | (Hz) |  |  |  |  | (Hz) |  | 

## Slide 59: Loop Optimization: Mathcad® Sheet
Compensator Transfet Function :
Comp( f , RH, RB, CA, RE, RS , CS)
ω 2.π.f
Z2 RS
1
ZH
i .CS.ω RH
KT
1 i .RH.CA.ω RB
RB ZH
ZT KT.ZH Z1
RE ZT A( f).Z2
A( f).Z1 Z1 Z2
.KT
k
CompM Comp f , RHm, RBm, CAm, REm, RSm, CSm
CompSk
k
Comp fk, RHs, RBs, CAs, REs , RSs , CSs
TS
TM. CompS
CompM
Amplifier Parameters :
A0 100.dB
fT 1.MHz
Common Variables or Functions :
fC
fT
A0
10 20
fC = 10 Hz
G_dB( X) 20.lg( X ).dB
A( f)
A0
10 20
1
i .
f fC
P_°( X)
arg( X)
deg
Loading Measurement :
Row0 = Fréeuency Row 1 = Gain (dB) Row 2 = Phase (°)
Measure
LIREPRN( Mes1)
NbV lignes( Measure)
NbV = 401
k 0 , 1 .. NbV 1
f Measure<0 >.Hz
GainV PhaseV
Measure<1 > Measure<2 > 180
TM 10
GainV
20
.ei .( PhaseV
180).deg

## Slide 60: Loop Optimization: Optimized Feedback
Here is new compensator used to boost phase and increase phase margin and bandwidth:
RH=19.75 kΩ RB=10 kΩ CA=680 pF RE=2.2 kΩ RS=10 kΩ CS=1 nF
Let’s compare and see the new open-loop plots …
Output
CS
RS
RB
RH
RE
CA
100dB/1MHz

## Slide 61: Loop Optimization: Feedback Comparison
New Feedback Phase Boost
 10
0
10
20
30
40
Measurement FB Gain (dB) Optimized Feedback
Gain(dB)
 90
 45
0
45
Measurement FB Phase (°) Optimized Feedback
Phase (°)
100 | 103 | Frequency | 104 | 105 | 100 | 103 | Frequency | 104 | 105
 |  | (Hz) |  |  |  |  | (Hz) |  | 

## Slide 62: Loop Optimization: Open-Loop Comparison
 40
 20
0
20
40
Measurement OL Gain (dB) Optimized Open-Loop
Gain(dB)
 180
 135
 90
 45
New Open-Loop Bandwidth New Open-Loop Phase Boost
60 0
Measurement OL Phase (°) Optimized Open-Loop
Phase (°)
100 | 103 Frequency | 104 | 105 | 100 | 103 | Frequency | 104 | 105
 | (Hz) |  |  |  |  | (Hz) |  | 

## Slide 63: Measurement Open-Loop Optimized Open-Loop
Loop Optimization: Open-Loop Comparison
Black-Nichols chart
-45°
+/-10dB
 180
 150
 120
 90
 60
 30
0
 40
 20
0
20
40
60
Gain(dB)
Phase (°)
New Phase Margin = 60°
45° minimum Phase Margin is maintained over
+/-10-dB Gain change
−1

## Slide 64: Conclusion
Public Information © onsemi 2022
Simulation versus Measurement

## Slide 65: Conclusion: Simulation versus Measurement
Most of the time, simulation and measurement are seen as two independent ways to obtain similar results…
Fans of both methods are fighting each other sometimes.
However, measurement is the only referee to verify simulation.

## Slide 66: Conclusion: Why Measuring the Loop ?
Measurements are real and you get the full system picture.
By measuring the loop, you integrate all parasitics and nonlinear effects.
You can check your calculus and margins.
You can assess the impact of input and output filters.

## Slide 67: Conclusion: Simulation AND Measurement
Simulation can be used during the design phase to predict system behaviors.
Measurements can be done for verifying design and fine-tuning the system in a real environment.
Simulation and measurements can be used together to bring a more complete system view.
Don’t rely only on one approach…
  Use Simulation AND Measurement !

## Slide 68
Follow Us @onsemi
www.onsemi.com